## Slide 1: Chapter 5
MSP432 ARM Timer Programming

## Slide 2: A 3-bit Counter

## Slide 3: An 8-bit up-counter stages

## Slide 4: An 8-bit down-counter stages

## Slide 5: Counting Events Using a Counter

## Slide 6: Using Counter as a Timer

## Slide 7: Capturing

## Slide 8: System Tick Timer Internal Structure

## Slide 9: STCTRL (System Tick Control)

## Slide 10: System Tick Counting

## Slide 11: STRVR vs. STCVR

## Slide 12: System Tick Timer Internal Structure

## Slide 13: Timer32 Registers
Offset | Acronym | Register Name | Type | Reset Value
00H | T32LOAD1 | Timer 1 Load Register | RW | 0
04H | T32VALUE1 | Timer 1 Current Value Register | R | FFFFFFFFH
08H | T32CONTROL1 | Timer 1 Timer Control Register | RW | 20H
0CH | T32INTCLR1 | Timer 1 Interrupt Clear Register | W | -
10H | T32RIS1 | Timer 1 Raw Interrupt Status Register | R | 0
14H | T32MIS1 | Timer 1 Interrupt Status Register | R | 0
18H | T32BGLOAD1 | Timer 1 Background Load Register | RW | 0
20H | T32LOAD2 | Timer 2 Load Register | RW | 0
24H | T32VALUE2 | Timer 2 Current Value Register | R | FFFFFFFFH
28H | T32CONTROL2 | Timer 2 Timer Control Register | RW | 20H
2CH | T32INTCLR2 | Timer 2 Interrupt Clear Register | W | -
30H | T32RIS2 | Timer 2 Raw Interrupt Status Register | R | 0
34H | T32MIS2 | Timer 2 Interrupt Status Register | R | 0
38H | T32BGLOAD2 | Timer 2 Background Load Register | RW | 0H

## Slide 14: T32CONTROLxRegister

## Slide 15: Counting in Free-Running Mode vs. Periodic Mode

## Slide 16: T32RIS Register

## Slide 17: T32LOAD vs. T32VALUE

## Slide 18: The Timer32 Prescaler

## Slide 19: Timer_A Simplified Diagram

## Slide 20: A more detailed diagram of Timer_A

## Slide 21: TAxR register

## Slide 22: TAxCTL register

## Slide 23: TAxCTL register
bit | Name | Description
0 | TAIFG | Timer_A Interrupt Flag 0: Timer did not overflow 1: Timer overflowed
1 | TAIE | Timer_A Interrupt Enable (0: Disabled, 1: Enabled)
2 | TACLR | Timer_A Clear
4-5 | MC | Mode Control: 00: Stop mode: timer is halted 01: Up mode: Timer counts up to TAxCCR0 10: Continuous mode: Timer counts up to 0xFFFF 11: Up/down mode: Timer counts up to TAxCCR0 then down to 0.
6-7 | ID | Input divider: These bits select the divider for the input clock: 00: divide by 1 01: divide by 2 10: divide by 4 11: divide by 8
8-9 | TASSEL | Timer_A clock Source Select: These bits select the Timer_A clock source: 00: TAxCLK (external clock): The timer uses external clock which is fed to the PM_TAxCLK pin. 01: ACLK (internal clock) 10: SMCLK (internal clock) 11: INCLK

## Slide 24: TAxCCRn Registers and TAxCCTLn Flags

## Slide 25: TAxCCRn Register

## Slide 26: TAxCCTLn Register

## Slide 27: TAxCCTLn Register (Table 17-6 of the chip manual)
bit | Name | Description
15-14 | CM | Capture mode 00: No capture 01: Capture on rising edge 10: Capture on falling edge 11: Capture on both rising and falling edges
13-12 | CCIS | Capture/compare input select. These its select the TAxCCR0 input signal: 00: CCIxA 01: CCIxB 10: GND 11: VCC
11 | SCS | Synchronize capture source. This bit is used to synchronize the capture input signal with the timer clock. 0: Asynchronous capture 1: Synchronous capture

## Slide 28: TAxCCTLn Register (Table 17-6 of the chip manual) (Cont.)
bit | Name | Description
10 | SCCI | Synchronized capture/compare input. The selected CCI input signal is latched with the EQUx signal and can be read via this bit.
8 | CAP | Capture mode 0: Compare mode 1: Capture mode
7-5 | OUTMOD | Output mode. Modes 2, 3, 6, and 7 are not useful for TAxCCR0 because EQUx = EQU0 000: OUT bit value 001: Set 010: Toggle/reset 011: Set/reset 100: Toggle 101: Reset 110: Toggle/set 111: Reset/set

## Slide 29: TAxCCTLn Register (Table 17-6 of the chip manual) (Cont.)
bit | Name | Description
4 | CCIE | Capture/compare interrupt enable. This bit enables the interrupt request of the corresponding CCIFG flag. 0: Interrupt disabled 1: Interrupt enabled
3 | CCI | Capture/compare input. The selected input signal can be read by this bit.
2 | OUT | Output. For output mode 0, this bit directly controls the state of the output. 0: Output low 1: Output high
1 | COV | Capture overflow. This bit indicates a capture overflow occurred. COV must be reset with software. 0: No capture overflow occurred 1: Capture overflow occurred
0 | CCIFG | Capture/compare interrupt flag 0: No interrupt pending 1: interrupt pending

## Slide 30: TAxEXn Register

## Slide 31: Counting in Up Mode

## Slide 32: Clock in Timer_A

## Slide 33: Continuous mode

## Slide 34: Input Edge Time Capturing

## Slide 35: TAxCCTLn Register

## Slide 36: TAxCCTLn Register (Table 17-6 of the chip manual)
bit | Name | Description
15-14 | CM | Capture mode 00: No capture 01: Capture on rising edge 10: Capture on falling edge 11: Capture on both rising and falling edges
13-12 | CCIS | Capture/compare input select. These its select the TAxCCR0 input signal: 00: CCIxA 01: CCIxB 10: GND 11: VCC
11 | SCS | Synchronize capture source. This bit is used to synchronize the capture input signal with the timer clock. 0: Asynchronous capture 1: Synchronous capture

## Slide 37: TAxCCTLn Register (Table 17-6 of the chip manual) (Cont.)
bit | Name | Description
10 | SCCI | Synchronized capture/compare input. The selected CCI input signal is latched with the EQUx signal and can be read via this bit.
8 | CAP | Capture mode 0: Compare mode 1: Capture mode
7-5 | OUTMOD | Output mode. Modes 2, 3, 6, and 7 are not useful for TAxCCR0 because EQUx = EQU0 000: OUT bit value 001: Set 010: Toggle/reset 011: Set/reset 100: Toggle 101: Reset 110: Toggle/set 111: Reset/set

## Slide 38: TAxCCTLn Register (Table 17-6 of the chip manual) (Cont.)
bit | Name | Description
4 | CCIE | Capture/compare interrupt enable. This bit enables the interrupt request of the corresponding CCIFG flag. 0: Interrupt disabled 1: Interrupt enabled
3 | CCI | Capture/compare input. The selected input signal can be read by this bit.
2 | OUT | Output. For output mode 0, this bit directly controls the state of the output. 0: Output low 1: Output high
1 | COV | Capture overflow. This bit indicates a capture overflow occurred. COV must be reset with software. 0: No capture overflow occurred 1: Capture overflow occurred
0 | CCIFG | Capture/compare interrupt flag 0: No interrupt pending 1: interrupt pending

## Slide 39: Choosing the Capture Edge
CM | Capture mode
00 | No capture
01 | Capture on rising edge
10 | Capture on falling edge
11 | Capture on both edges

## Slide 40: Port pin assignement of Timer_A
Timer_A | Port Pin | Timer_A | Port Pin | Timer_A | Port Pin | Timer_A | Port Pin
TA0.0 | P7.3 | TA1.0 | P8.0 | TA2.0 | P8.1 | TA3.0 | P10.4
TA0.1 | P2.4 | TA1.1 | P7.7 | TA2.1 | P5.6 | TA3.1 | P10.5
TA0.2 | P2.5 | TA1.2 | P7.6 | TA2.2 | P5.7 | TA3.2 | P8.2
TA0.3 | P2.6 | TA1.3 | P7.5 | TA2.3 | P6.6 | TA3.3 | P9.2
TA0.4 | P2.7 | TA1.4 | P7.4 | TA2.4 | P6.7 | TA3.4 | P9.3

## Slide 41: Measuring Period and Pulse Width