## Slide 1: Chapter 6
Interrupt and Exception Programming

## Slide 2: Polling vs. Interrupts

## Slide 3: NVIC in ARM Cortex-M

## Slide 4: Interrupt Vector Table for ARM Cortex-M
Interrupt # | Interrupt | Memory Location (Hex)
 | Stack Pointer initial value | 0x00000000
1 | Reset | 0x00000004
2 | NMI | 0x00000008
3 | Hard Fault | 0x0000000C
4 | Memory Management Fault | 0x00000010
5 | Bus Fault | 0x00000014
6 | Usage Fault (undefined instructions, divide by zero, unaligned memory access,...) | 0x00000018
7 | Reserved | 0x0000001C
8 | Reserved | 0x00000020
9 | Reserved | 0x00000024
10 | Reserved | 0x00000028
11 | SVCall | 0x0000002C
12 | Debug Monitor | 0x00000030
13 | Reserved | 0x00000034
14 | PendSV | 0x00000038
15 | SysTick | 0x0000003C
16 | IRQ 0 for peripherals | 0x00000040
17 | IRQ 1 for peripherals | 0x00000044
… | … | …
255 | IRQ 239 for peripherals | 0x000003FC

## Slide 5: Going from Reset to Boot Program

## Slide 6: ARM Cortex-M Stack Frame upon Interrupt

## Slide 7: Main Program gets interrupted

## Slide 8: Interrupt Priority for ARM Cortex-M
Interrupt # | Interrupt | Priority Level
0 | Stack Pointer initial value | 
1 | Reset | -3 Highest
2 | NMI | -2
3 | Hard Fault | -1
4 | Memory Management Fault | Programmable
5 | Bus Fault | Programmable
6 | Usage Fault (undefined instructions, divide by zero, unaligned memory access,....) | Programmable
7 | Reserved | Programmable
8 | Reserved | Programmable
9 | Reserved | Programmable
10 | Reserved | Programmable
11 | SVCall | Programmable
12 | Debug Monitor | Programmable
13 | Reserved | Programmable
14 | PendSV | Programmable
15 | SysTick | Programmable
16 | IRQ 0 for peripherals | Programmable
17 | IRQ 1 for peripherals | Programmable
… | … | Programmable
255 | IRQ 239 for peripherals | Programmable

## Slide 9: CONTROL Register in ARM Cortex-M4
nPRIV (Privilege): Defines the Thread mode privilege level 0: Privileged 1: Unprivileged Active Stack Pointer (ASP): Defines the currently active stack pointer (ASP = SPSEL) 0: MSP is the current stack pointer. 1: PSP is the current stack pointer. Floating Point Context Active (FPCA) 0: No floating point context active. 1: Floating point context active.

## Slide 10: Privileged level Execution and Processor Modes in ARM Cortex-M
Processor Mode | Software | Privilege level
Thread | Applications | Privileged and Unprivileged
Handler | ISR for Exceptions and IRQs | Always Privileged
In Thread mode, use bit 0 of the CONTROL register to select Privileged or Unprivileged |  | 

## Slide 11: Processor Modes and Stack Usage in ARM Cortex-M
Processor Mode | Software | Stack Usage
Thread | Applications | MSP or PSP
Handler | ISR for Exceptions and IRQs | MSP
Note: In Thread mode, use bit 1 of the Control register to select MSP or PSP for stack pointer. |  | 

## Slide 12: Processor Mode, Privilege, and Stack in ARM Cortex
Mode | Privilege | Stack Pointer | Typical Example usage
Handler | Privileged | Main | Exception Handling
Handler | Unprivileged | Any | Reserved since Handler is always Privileged
Thread | Privileged | Main | Operating system kernel
Thread | Privileged | Process | 
Thread | Unprivileged | Main | 
Thread | Unprivileged | Process | Application threads

## Slide 13: ARM Cortex-M Registers

## Slide 14: Special function registers of ARM Cortex-M
Register name | Privilege Usage
MSP (main stack pointer) | Privileged
PSP (processor stack pointer) | Privileged or Unprivileged
PSR (Processor status register) | Privileged
APSR (application processor status register) | Privileged or Unprivileged
ISPR (interrupt processor status register) | Privileged
EPSR (execution processor status register) | Privileged
PRIMASK (Priority Mask register) | Privileged
FAULTMASK(fault mask register) | Privileged
BASEPRI (base priority register) | Privileged
CONTROL (control register) | Privileged
Note: We must use MSR and MRS instructions to access the above registers | 

## Slide 15: IRQ assignment in MSP432P401R
INT# | IRQ# | Vector location | Device
1-15 | None | 0000 0000 to 0000 003C | CPU Exception(set by ARM)
16 | 0 | 0000 0040 | PSS
17 | 1 | 0000 0044 | CS
18 | 2 | 0000 0048 | PCM
19 | 3 | 0000 004C | WDT_A
20 | 4 | 0000 0050 | FPU_INT
21 | 5 | 0000 0054 | Flash Controller
22 | 6 | 0000 0058 | COMP_E1
23 | 7 | 0000 005C | COMP_E2
24 | 8 | 0000 0060 | TIMERA0
25 | 9 | 0000 0064 | TIMERA0
26 | 10 | 0000 0068 | TIMERA1
27 | 11 | 0000 006C | TIMERA1
28 | 12 | 0000 0070 | TIMERA2

## Slide 16: IRQ assignment in MSP432P401R (Cont.)
INT# | IRQ# | Vector location | Device
29 | 13 | 0000 0074 | TIMERA2
30 | 14 | 0000 0078 | TIMERA3
31 | 15 | 0000 007C | TIMERA3
32 | 16 | 0000 0080 | eUSCI_A0
33 | 17 | 0000 0084 | eUSCI_A1
34 | 18 | 0000 0088 | eUSCI_A2
35 | 19 | 0000 008C | eUSCI_A3
36 | 20 | 0000 0090 | eUSCI_B0
37 | 21 | 0000 0094 | eUSCI_B1
38 | 22 | 0000 0098 | eUSCI_B3
39 | 23 | 0000 009C | eUSCI_B4
40 | 24 | 0000 00A0 | ADC14
41 | 25 | 0000 00A4 | TIMER32_INT1
42 | 26 | 0000 00A8 | TIMER32_INT2

## Slide 17: IRQ assignment in MSP432P401R (Cont.)
INT# | IRQ# | Vector location | Device
43 | 27 | 0000 00AC | TIMER32_INTC
44 | 28 | 0000 00B0 | AES256
45 | 29 | 0000 00B4 | RTC_C
46 | 30 | 0000 00B8 | DMA_ERR
47 | 31 | 0000-00BC | DMA_INT3
48 | 32 | 0000 00C0 | DMA_INT2
49 | 33 | 0000 00C4 | DMA_INT1
50 | 34 | 0000 00C8 | DMA_INT0
51 | 35 | 0000-00CC | I/O Port P1
52 | 36 | 0000 00D0 | I/O Port P2
53 | 37 | 0000 00D4 | I/O Port P3
54 | 38 | 0000 00D8 | I/O Port P4
55 | 39 | 0000-00DC | I/O Port P5
56 | 40 | 0000 00E0 | I/O Port P6
57-79 | 41-63 | 0000 00E4 – 0000 013C | reserved

## Slide 18: Interrupt enabling at all 3 levels

## Slide 19: PxIE register

## Slide 20: Interrupts 0–31 Set Enable (EN0)

## Slide 21: Interrupts 0–31 Clear Enable (DIS0)

## Slide 22: Enabling and Disabling an Interrupt

## Slide 23: PxIES Interrupt edge activation bits

## Slide 24: UART Interrupt Registers

## Slide 25: UCAxIE (UARTx Interrupt Enable) register
Field | Bit | Description
UCTXCPTIE | D3 | Transmit complete interrupt enable 0 = Interrupt disabled 1 = Interrupt enabled
UCSTTIE | D2 | Start bit interrupt enable 0 = Interrupt disabled 1 = Interrupt
UCTXIE | D1 | Transmit interrupt enable 0 = Interrupt disabled 1 = Interrupt enabled
UCRXIE | D0 | Receive interrupt enable 0 = Interrupt disabled 1 = Interrupt enabled

## Slide 26: SysTick Internal Structure

## Slide 27: SysTick Control and Status Register (STCTRL)

## Slide 28: SysTick Counting

## Slide 29: IE (Interrupt Enable) bit (d5) in T32CONTROLx (T32 Control) register

## Slide 30: Making Periodic Interrupts using Timer_A

## Slide 31: IPRn Registers