## Slide 1: Chapter 7
ADC, DAC, and Sensor Interfacing

## Slide 2: Microcontroller Connection to Sensor via ADC

## Slide 3: An 8-bit ADC Block Diagram

## Slide 4: Resolution versus Step Size for ADC (Vref = 5V)
n-bit | Number of steps | Step size
8 | 256 | 5V /256 = 19.53 mV
10 | 1024 | 5V /1024 = 4.88 mV
12 | 4096 | 5V /4096 = 1.2 mV
16 | 65,536 | 5V /65,536 = 0.076 mV
Note: Vref = 5V |  | 

## Slide 5: Vref Relation to Vin Range for an 8-bit ADC
Vref (V) | Vin in Range (V) | Step Size (mV)
5.00 | 0 to 5 | 5 / 256 = 19.53
4.00 | 0 to 4 | 4 / 256 = 15.62
3.00 | 0 to 3 | 3 / 256 = 11.71
2.56 | 0 to 2.56 | 2.56 / 256 = 10
2.00 | 0 to 2 | 2 / 256 = 7.81
1.28 | 0 to 1.28 | 1.28 / 256 = 5
1.00 | 0 to 1 | 1 / 256 = 3.90
Note: In an 8-bit ADC, step size is Vref/256 |  | 

## Slide 6: Vref Relation to Vin Range for an 10-bit ADC
Vref (V) | VinRange (V) | Step Size (mV)
5.00 | 0 to 5 | 5 / 1024 = 4.88
4.96 | 0 to 4.096 | 4.096 / 1024 = 4
3.00 | 0 to 3 | 3 / 1024 = 2.93
2.56 | 0 to 2.56 | 2.56 / 1024 = 2.5
2.00 | 0 to 2 | 2 / 1024 = 2
1.28 | 0 to 1.28 | 1.28 / 1024 = 1.25
1.024 | 0 to 1.024 | 1.024 / 1024 = 1
Note: In a 10-bit ADC, step size is Vref/1024 |  | 

## Slide 7: A Simultaneous 2-bit ADC

## Slide 8: ADC0848 Parallel ADC Block Diagram

## Slide 9: MAX1112 Serial ADC Block Diagram

## Slide 10: Successive Approximation ADC

## Slide 11: Simplified Block Diagram of MSP432P401R chip

## Slide 12: Some of the MSP432P401R ADC Registers (See reference manual table 20-3)
Absolute Address | Register
4001 2000 | ADC Control Registers 0 (ADC14CTL0)
4001 2004 | ADC Control Registers 1 (ADC14CTL1)
4001 2018 | ADC Memory Control Register0 (ADC14MCTL0, there are 32 of them)
4001 2098 | ADC Memory Register0 (ADC14M0, there are 32 of them)
4001 213C | ADC IER0 Register (ADC14 Interrupt Enable 0)
4001 2144 | ADC IFGR0 (ADC14 Interrupt Flag 0)

## Slide 13: ADC14CTL0 (ADC14 Control 0) register

## Slide 14: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R
Bit | Field | Descriptions
31-30 | ADC14PDIV | ADC14 predivider. These bits pre-divides the selected ADC14 clock source. Can be modified only when ADC14ENC = 0. 00b = Predivide by 1 01b = Predivide by 4 10b = Predivide by 32 11b = Predivide by 64
29-27 | ADC14SHSx | ADC14 sample-and-hold source select. Can be modified only when ADC14ENC = 0. 000b = ADC14SC bit 001b = TA0_C1 010b = TA0_C2 011b = TA1_C1 100b = TA1_C2 101b = TA2_C1 110b = TA2_C2 111b = TA3_C1

## Slide 15: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
26 | ADC14SHP | ADC14 sample-and-hold pulse-mode select. This bit selects the source of the sampling signal (SAMPCON) to be either the output of the sampling timer or the sample-input signal directly. Can be modified only when ADC14ENC = 0. 0b = SAMPCON signal is sourced from the sample-input signal. 1b = SAMPCON signal is sourced from the sampling timer
25 | ADC14ISSH | ADC14 invert signal sample-and-hold. Can be modified only when ADC14ENC = 0. 0b = The sample-input signal is not inverted. 1b = The sample-input signal is inverted. Setting ADC14ISSH=1 and triggering a conversion using ADC14SC is not recommended. ADC14SC bit gets reset to 0 automatically at the end of conversion and if ADC14ISSH=1, the 1->0 transition on ADC14SC will trigger another conversion.

## Slide 16: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
24-22 | ADC14DIVx | ADC14 clock divider. Can be modified only when ADC14ENC = 0. 000b = /1 001b = /2 010b = /3 011b = /4 100b = /5 101b = /6 110b = /7 111b = /8

## Slide 17: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
21-19 | ADC14SSELx | ADC14 clock source select. Can be modified only when ADC14ENC = 0. 000b = MODCLK 001b = SYSCLK 010b = ACLK 011b = MCLK 100b = SMCLK 101b = HSMCLK 110b = Reserved 111b = Reserved
18-17 | ADC14CONSEQx | ADC14 conversion sequence mode select Can be modified only when ADC14ENC=0. 00b = Single-channel, single-conversion 01b = Sequence-of-channels 10b = Repeat-single-channel 11b = Repeat-sequence-of-channels

## Slide 18: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
16 | ADC14BUSY | ADC14 busy. This bit indicates an active sample or conversion operation. 0b = No operation is active. 1b = A sequence, sample, or conversion is active
15-12 | ADC14SHT1x | ADC14 sample-and-hold time. These bits define the number of ADC14CLK cycles in the sampling period for registers ADC14MEM8 to ADC14MEM23. Can be modified only when ADC14ENC = 0. 0000b = 4 0001b = 8 0010b = 16 0011b = 32 0100b = 64 0101b = 96 0110b = 128 0111b = 192 1000b to 1111b = Reserved

## Slide 19: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
11-8 | ADC14SHT0x | ADC14 sample-and-hold time. These bits define the number of ADC14CLK cycles in the sampling period for registers ADC14MEM0 to ADC14MEM7 and ADC14MEM24 to ADC14MEM31. Can be modified only when ADC14ENC = 0. 0000b = 4 0001b = 8 0010b = 16 0011b = 32 0100b = 64 0101b = 96 0110b = 128 0111b = 192 1000b to 1111b = Reserved

## Slide 20: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
7 | ADC14MSC | ADC14 multiple sample and conversion. Valid only for sequence or repeated modes. 0b = The sampling timer requires a rising edge of the SHI signal to trigger each sample-and-convert. 1b = The first rising edge of the SHI signal triggers the sampling timer, but further sample-and-conversions are performed automatically as soon as the prior conversion is completed
6-5 | Reserved | Reserved. Always reads as 0.
4 | ADC14ON | ADC14 on 0b = ADC14 off 1b = ADC14 on. ADC core is ready to power up when a valid conversion is triggered.

## Slide 21: ADC14CTL0 (ADC14 Control 0) Register of MSP432P401R (Cont.)
Bit | Field | Descriptions
3-2 | Reserved | Reserved. Always reads as 0.
1 | ADC14ENC | ADC14 enable conversion 0b = ADC14 disabled 1b = ADC14 enabled ADC14ENC low pulse width must be at-least 3 ADC14CLK cycles.
0 | ADC14SC | ADC14 start conversion. Software-controlled sample-and-conversion start. ADC14SC and ADC14ENC may be set together with one instruction. ADC14SC is reset automatically. 0b = No sample-and-conversion-start 1b = Start sample-and-conversion

## Slide 22: ADC14MCTL0 Register

## Slide 23: ADC14MCTL0 Register
Bit | Field | Description
13 | ADC14DIF | Differential mode (0= single-ended, 1=Differential)
11-18 | ADCVRSEL | ADC14 Vref selection. 0000 = Vref+= AVCC (analog VCC) and Vref-=AVSS 1110 = Vref+= External Source connected to pin P5.6 Vref- =External Source connected to pin P5.7
4-0 | ADC14INCH | ADC14 input channel: The field selects the input channel. When DIFF = 0 (single-ended mode), values 0 to 23 choose between the 24 ADC input channels. When DIFF = 1 (Differential mode), values 0 to 15 select between the 12 differential channels. See the reference manual for more information. 00000 = A0 00001 = A1 … 10111 = A23

## Slide 24: Analog input pin assignment in MSP432P401R chip for LaunchPad
Pin Function | ADC Channel Input | Pin Name | PxSEL1 : PxSEL0
A0 | ADC input 0 | P5.5 | P5SEL0=00100000=0x20 & P5SEL1=00100000=0x20
A1 | ADC input 1 | P5.4 | P5SEL0=00010000=0x10 & P5SEL1=00010000=0x10
A2 | ADC input 2 | P5.3 | P5SEL0=00001000=0x08 & P5SEL1=00001000=0x08
A3 | ADC input 3 | P5.2 | P5SEL0=00000100=0x04 & P5SEL1=00000100=0x04
A4 | ADC input 4 | P5.1 | P5SEL0=00000010=0x02 & P5SEL1=00000010=0x02
A5 | ADC input 5 | P5.0 | P5SEL0=00000001=0x01 & P5SEL1=00000001=0x01
A6 | ADC input6 | P4.7 | P4SEL0=10000000=0x80 & P4SEL1=10000000=0x80
A7 | ADC input 7 | P4.6 | P4SEL0=01000000=0x40 & P4SEL1=01000000=0x40
A8 | ADC input 8 | P4.5 | P4SEL0=00100000=0x20 & P4SEL1=00100000=0x20
A9 | ADC input 9 | P4.4 | P4SEL0=00010000=0x10 & P4SEL1=00010000=0x10
A10 | ADC input 10 | P4.3 | P4SEL0=00001000=0x08 & P4SEL1=00001000=0x08
A11 | ADC input 11 | P4.2 | P4SEL0=00000100=0x04 & P4SEL1=00000100=0x04
A12 | ADC input 12 | P4.1 | P4SEL0=00000010=0x02 & P4SEL1=00000010=0x02

## Slide 25: Analog input pin assignment in MSP432P401R chip for LaunchPad (Cont.)
Pin Function | ADC Channel Input | Pin Name | PxSEL1 : PxSEL0
A13 | ADC input 13 | P4.0 | P4SEL0=00000001=0x01 & P4SEL1=00000001=0x01
A14 | ADC Input 14 | P6.1 | P6SEL0=00000010=0x02 & P6SEL1=00000010=0x02
A15 | ADC Input 15 | P6.0 | P6SEL0=00000001=0x01 & P6SEL1=00000001=0x01
A16 | ADC Input 16 | P9.1 | P9SEL0=00000010=0x02 & P9SEL1=00000010=0x02
A17 | ADC Input 17 | P9.0 | P9SEL0=00000001=0x01 & P9SEL1=00000001=0x01
A18 | ADC Input 18 | P8.7 | P8SEL0=10000000=0x80 & P8SEL1=10000000=0x80
A19 | ADC Input 19 | P8.6 | P8SEL0=01000000=0x40 & P8SEL1=01000000=0x40
A20 | ADC Input 20 | P8.5 | P8SEL0=00100000=0x20 & P8SEL1=00100000=0x20
A21 | ADC Input 21 | P8.4 | P8SEL0=00010000=0x10 & P8SEL1=00010000=0x10
A22 | ADC Input 22 | P8.3 | P8SEL0=00001000=0x08 & P8SEL1=00001000=0x08
A23 | ADC Input 23 | P8.2 | P8SEL0=00000100=0x04 & P8SEL1=00000100=0x04

## Slide 26: ADC14CTL1 (ADC14 Control 1) Register

## Slide 27: ADC14CTL1 (ADC14 Control 1) Register
Bit | Name | Description
31-28 | Reserved | Reserved
27 | ADC14CH3MAP | 0b = ADC input channel internal 3 is not selected 1b = ADC input channel internal 3 is selected for ADC input channel MAX-5
26 | ADC14CH2MAP | 0b = ADC input channel internal 2 is not selected 1b = ADC input channel internal 2 is selected for ADC input channel MAX-4
25 | ADC14CH1MAP | 0b = ADC input channel internal 1 is not selected 1b = ADC input channel internal 1 is selected for ADC input channel MAX-3
24 | ADC14CH0MAP | 0b = ADC input channel internal 0 is not selected 1b = ADC input channel internal 0 is selected for ADC input channel MAX-2
23 | ADC14TCMAP | 0b = ADC internal temperature sensor channel is not selected for ADC 1b = ADC internal temperature sensor channel is selected for ADC input channel
22 | ADC14BATMAP | 0b = ADC internal 1/2 x AVCC channel is not selected for ADC 1b = ADC internal 1/2 x AVCC channel is selected for ADC input channel MAX

## Slide 28: ADC14CTL1 (ADC14 Control 1) Register (Cont.)
Bit | Name | Description
21 | Reserved | Reserved
20-16 | ADC14CSTARTADDx | 0h to 1Fh, corresponding to ADC14MEM0 to ADC14MEM31
15-6 | Reserved | Reserved
5-4 | ADC14RES | 00b = 8 bit (9 clock cycle conversion time) 01b = 10 bit (11 clock cycle conversion time) 10b = 12 bit (14 clock cycle conversion time) 11b = 14 bit (16 clock cycle conversion time)

## Slide 29: ADC14CTL1 (ADC14 Control 1) Register (Cont.)
Bit | Name | Description
3 | ADC14DF | 0b = Binary unsigned. Theoretically, for ADC14DIF = 0 and 14-bit mode, the analog input voltage - V(REF) results in 0000h, and the analog input voltage + V(REF) results in 3FFFh. 1b = Signed binary (2s complement), left aligned. Theoretically, for ADC14DIF = 0 and 14-bit mode, the analog input voltage - V(REF) results in 8000h, and the analog input voltage + V(REF) results in 7FFCh.
2 | ADC14REFBURST | 0b = ADC reference buffer on continuously 1b = ADC reference buffer on only during sample-and-conversion
1-0 | ADC14PWRMD | 00b = Regular power mode for use with any resolution setting. Sample rate can be up to 1 Msps. 01b = Reserved 10b = Low-power mode for 12-bit, 10-bit, and 8-bit resolution settings. Sample rate must not exceed 200 ksps. 11b = Reserved

## Slide 30: ADC14IFGR0 (ADC14 Interrupt Flag Register 0) Register for End-of-Conversion

## Slide 31: ADC14IFGR0 Register
Bit | Field | Descriptions
x | ADC14IFGx | ADC14MEMx interrupt flag. This bit is set to 1 when ADC14MEMx is loaded with a conversion result. This bit is reset to 0 when the ADC14MEMx register is read, or when the ADC14IV register is read, or when the corresponding bit in the ADC14CLRIFGR0 register is set to 1. 0b = No interrupt pending 1b = Interrupt pending

## Slide 32: ADC14MEMx (ADC14 memoryx) holding ADC14 conversion result (x=0- 31)

## Slide 33: ADC Connection for Program 7-1

## Slide 34: Thermistor Resistance vs. Temperature
Temperature ('C) | Tf (K ohms)
0 | 29.490
25 | 10.000
50 | 3.893
75 | 1.700
100 | 0.817

## Slide 35: Thermistor (Copied from http://www.maximintegrated.com)

## Slide 36: LM34 and LM35

## Slide 37: Getting analog data to the CPU

## Slide 38: LM34/35 Connection to ARM and Its Pin Configuration

## Slide 39: DAC Block Diagram

## Slide 40: Microcontroller Connection to DAC0808

## Slide 41: Saw Tooth Wave Form

## Slide 42: Angle vs. Voltage Magnitude for Sine Wave
Angle Ɵ (degrees) | Sin Ɵ | VOUT (Voltage Magnitude) 5V + (5V × sin Ɵ) | Values Sent to DAC (decimal) (Voltage Mag. × 25.6)
0 | 0 | 5 | 128
30 | 0.5 | 7.5 | 192
60 | 0.866 | 9.33 | 238
90 | 1.0 | 10 | 255
120 | 0.866 | 9.33 | 238
150 | 0.5 | 7.5 | 192
180 | 0 | 5 | 128
210 | -0.5 | 2.5 | 64
240 | -0.866 | 0.669 | 17
270 | -1.0 | 0 | 0
300 | -0.866 | 0.669 | 17
330 | -0.5 | 2.5 | 64
360 | 0 | 5 | 128

## Slide 43: Angle vs. Voltage Magnitude for Sine Wave