## Slide 1: Chapter 8
SPI Protocol and DAC Interfacing

## Slide 2: SPI Bus vs. Traditional Parallel Bus Connection to Microcontroller

## Slide 3: SPI Architecture

## Slide 4: SPI Clock Polarity and phase

## Slide 5: SPI Clock Polarity and phase
Clock Polarity | Clock Phase | Data read and change time | SPI Mode
0 | 0 | read on falling edge, changed on a rising edge | 0
0 | 1 | read on rising edge, changed on a falling edge | 1
1 | 0 | read on rising edge, changed on a falling edge | 2
1 | 1 | read on falling edge, changed on a rising edge | 3

## Slide 6: eUSCI_A Module Base Address (Shared with UART)
USCI_Ax Module | Base Address
eUSCI_A0 | 0x4000_1000
eUSCI_A1 | 0x4000_1400
eUSCI_A2 | 0x4000_1800
eUSCI_A3 | 0x4000_1C00

## Slide 7: eUSCI_B Module Base Address (Shared with I2C)
USCI_Bx Module | Base Address
eUSCI_B0 | 0x4000_2000
eUSCI_B1 | 0x4000_2400
eUSCI_B2 | 0x4000_2800
eUSCI_B3 | 0x4000_2C00

## Slide 8: eUSCI Registers
Register Name | Register Function
UCAxCTLW0 (UCAx Control Word 0) | Control 0
UCAxBRW (UCAx Baud Rate Control Word) | Baud Rate
UCAxSTATW (UCAx Status) | Status
UCAxRXBUF (UCAx Receive Buffer) | Receive Register
UCAxTXBUF (UCAx Transmit Buffer) | Transmit Register
UCAxIE (UCAx Interrupt Enable) | Interrupt Enable
UCAxIFG (UCAx Interrupt Flag) | Interrupt Flags
UCAxIV (UCAx Interrupt Vector) | Interrupt Vector

## Slide 9: SPI Control Word 0 (UCAxCTLW0) Registers in MSP432

## Slide 10: UCAxCTLW0 (UCAx Control Word 0) register
Bits | Name | Function | Description
0 | UCSWRST | Software reset enable | 0b = Disabled. eUSCI reset released for operation. 1b = Enabled. eUSCI logic held in reset state
1 | UCSTEM | STE mode select in master mode. | 0b = STE pin is used to prevent conflicts with other masters 1b = STE pin is used to generate the enable signal for a 4-wire slave
7-6 | UCSSELx | eUSCI clock source select | 00b = Reserved 01b = ACLK 10b = SMCLK 11b = SMCLK
8 | UCSYNC | Synchronous mode enable | 0b = Asynchronous mode (UART) 1b = Synchronous mode (SPI or I2C)
10-9 | UCMODEx | eUSCI mode. | 00b = 3-pin SPI 01b = 4-pin SPI with UCxSTE active high: Slave enabled when UCxSTE = 1 10b = 4-pin SPI with UCxSTE active low: Slave enabled when UCxSTE = 0 11b = I2C mode

## Slide 11: UCAxCTLW0 (UCAx Control Word 0) register (Cont.)
Bits | Name | Function | Description
11 | UCMST | Master mode select | 0b = Slave mode 1b = Master mode
12 | UC7BIT | Character length | 0b = 8-bit data 1b = 7-bit data
13 | UCMSB | MSB first select. | 0b = LSB first 1b = MSB first
14 | UCCKPL | Clock polarity select | 0b = The inactive state is low. 1b = The inactive state is high.
15 | UCCKPH | Clock phase select | 0b = Data is changed on the first UCLK edge and captured on the following edge. 1b = Data is captured on the first UCLK edge and changed on the following edge.

## Slide 12: Using MSP432 SPI module as Master

## Slide 13: UCAxBRW Register SPI Baud Rate

## Slide 14: UCAxTXDBUF register

## Slide 15: UCAxRXDBUF register

## Slide 16: UCAx Status (UCAxSTATW) Register

## Slide 17: UCAx Status (UCAxSTATW) Register
Bits | Name | Function | Description
0 | UCBUSY | SPI Busy Bit | The bit is 1 when the SPI is currently busy transmitting or receiving
5 | UCOE | Overrun error flag. | 0b = No error 1b = Overrun error occurred
6 | UCFE | Framing error flag. | 0b = No error 1b = Bus conflict occurred
7 | UCLISTEN | Listen enable. | 0b = Disabled 1b = Enabled. The transmitter output is internally fed back to the receiver.

## Slide 18: UCAx Interrupt Flag (UCAxIFG) Register

## Slide 19: UCAx Interrupt Flag (UCAxIFG) Register
Bits | Name | Function | Description
0 | UCRXIFG | RX Receive Interrupt flag | The bit is 1 when the receive BUF is empty
1 | UCTXIFG | TX Transmit Interrupt flag | The bit is 1 when the transmit BUF is empty

## Slide 20: IO Pin Assignment for all 4 UCAx Modules
SPI Module Pin | IO Pin | SPI Module Pin | IO Pin
STE(UCA0) | P1.0 | STE(UCA1) | P2.0
CLK(UCA0) | P1.1 | CLK(UCA1) | P2.1
SOMI(UCA0) | P1.2 | SOMI(UCA1) | P2.2
SIMO(UCA0) | P1.3 | SIMO(UCA1) | P2.3
STE(UCA2) | P3.0 | STE(UCA3) | P9.4
CLK(UCA2) | P3.1 | CLK(UCA3) | P9.5
SOMI(UCA2) | P3.2 | SOMI(UCA3) | P9.6
SIMO(UCA2) | P3.3 | SIMO(UCA3) | P9.7

## Slide 21: IO Pin Assignment for all 4 UCBx Modules
SPI Module Pin | IO Pin | SPI Module Pin | IO Pin
STE(UCB0) | P1.4 | STE(UCB1) | P6.2
CLK(UCB0) | P1.5 | CLK(UCB1) | P6.3
SIMO(UCB0) | P1.6 | SIMO(UCB1) | P6.4
SOMI(UCB0) | P1.7 | SOMI(UCB1) | P6.5
STE(UCB2) | P3.4 | STE(UCB3) | P10.0
CLK(UCB2) | P3.5 | CLK(UCB3) | P10.1
SIMO(UCB2) | P3.6 | SIMO(UCB3) | P10.2
SOMI(UCB2) | P3.7 | SOMI(UCB3) | P10.3

## Slide 22: Pins available for UCAs
I/O pin | Function | PxSEL1=0 | PxSEL0=1
P1.0 | STE(UCA0) | P1SEL1=00000000 | P1SEL0=00000001
P1.1 | CLK(UCA0) | P1SEL1=00000000 | P1SEL0=00000010
P1.2 | SOMI(UCA0) | P1SEL1=00000000 | P1SEL0=00000100
P1.3 | SIMO(UCA0) | P1SEL1=00000000 | P1SEL0=00001000
For SPI0: |  | P1SEL1=0x00 | P1SEL0=00001111=0x0F
P2.0 | STE(UCA1) | P2SEL1=00000000 | P2SEL0=00000001
P2.1 | CLK(UCA1) | P2SEL1=00000000 | P2SEL0=00000010
P2.2 | SOMI(UCA1) | P2SEL1=00000000 | P2SEL0=00000100
P2.3 | SIMO(UCA1) | P2SEL1=00000000 | P2SEL0=00001000
For SPI1: |  | P2SEL1=0x00 | P2SEL0=00001111=0x0F
P3.0 | STE(UCA2) | P3SEL1=00000000 | P3SEL0=00000001
P3.1 | CLK(UCA2) | P3SEL1=00000000 | P3SEL0=00000010
P3.2 | SOMI(UCA2) | P3SEL1=00000000 | P3SEL0=00000100
P3.3 | SIMO(UCA2) | P3SEL1=00000000 | P3SEL0=00001000
For SPI2: |  | P3SEL1=0x00 | P3SEL0=00001111=0x0F
P9.4 | STE(UCA3) | P9SEL1=00000000 | P9SEL0=00010000
P9.5 | CLK(UCA3) | P9SEL1=00000000 | P9SEL0=00100000
P9.6 | SOMI(UCA3) | P9SEL1=00000000 | P9SEL0=01000000
P9.7 | SIMO(UCA3) | P9SEL1=00000000 | P9SEL0=10000000
For SPI3: |  | P9SEL1=0x00 | P9SEL0=11110000=0xF0

## Slide 23: Pins available for UCBs
I/O pin | Function | PxSEL1=0 | PxSEL0=1
P1.4 | STE(UCB0) | P1SEL1=00000000 | P1SEL0=00010000
P1.5 | CLK(UCB0) | P1SEL1=00000000 | P1SEL0=00100000
P1.6 | SIMO(UCB0) | P1SEL1=00000000 | P1SEL0=01000000
P1.7 | SOMI(UCB0) | P1SEL1=00000000 | P1SEL0=10000000
For SPI0: |  | P1SEL1=0x00 | P1SEL0=11110000=0XF0
P6.2 | STE(UCB1) | P2SEL1=00000000 | P2SEL0=00000100
P6.3 | CLK(UCB1) | P6SEL1=00000000 | P6SEL0=00001000
P6.4 | SIMO(UCB1) | P6SEL1=00000000 | P6SEL0=00010000
P6.5 | SOMI(UCB1) | P6SEL1=00000000 | P6SEL0=00100000
For SPI1: |  | P6SEL1=0x00 | P6SEL0=00111100=0x3C
P3.4 | STE(UCB2) | P3SEL1=00000000 | P3SEL0=00010000
P3.5 | CLK(UCB2) | P3SEL1=00000000 | P3SEL0=00100000
P3.6 | SIMO(UCB2) | P3SEL1=00000000 | P3SEL0=01000000
P3.7 | SOMI(UCB2) | P3SEL1=00000000 | P3SEL0=10000000
For SPI2: |  | P3SEL1=0x00 | P3SEL0=11110000=0xF0
P10.0 | STE(UCB3) | P10SEL1=00000000 | P10SEL0=00000001
P10.1 | CLK(UCB3) | P10SEL1=00000000 | P10SEL0=00000010
P10.2 | SIMO(UCB3) | P10SEL1=00000000 | P10SEL0=00000100
P10.3 | SOMI(UCB3) | P10SEL1=00000000 | P10SEL0=00001000
For SPI3: |  | P10SEL1=0x00 | P10SEL0=00001111=0x0F

## Slide 24: eUSCI_B Module Base Address (Shared with I2C)
USCI_Bx Module | Base Address
eUSCI_B0 | 0x4000_2000
eUSCI_B1 | 0x4000_2400
eUSCI_B2 | 0x4000_2800
eUSCI_B3 | 0x4000_2C00

## Slide 25: IO Pin Assignment for all 4 UCBx Modules
SPI Module Pin | IO Pin | SPI Module Pin | IO Pin
STE(UCB0) | P1.4 | STE(UCB1) | P6.2
CLK(UCB0) | P1.5 | CLK(UCB1) | P6.3
SIMO(UCB0) | P1.6 | SIMO(UCB1) | P6.4
SOMI(UCB0) | P1.7 | SOMI(UCB1) | P6.5
STE(UCB2) | P3.4 | STE(UCB3) | P10.0
CLK(UCB2) | P3.5 | CLK(UCB3) | P10.1
SIMO(UCB2) | P3.6 | SIMO(UCB3) | P10.2
SOMI(UCB2) | P3.7 | SOMI(UCB3) | P10.3

## Slide 26: SPI pins for UCAx and UCBx

## Slide 27: LTC1661 Internal Block Diagram

## Slide 28: Sending a Packet of Data to LTC166x

## Slide 29: LTC1661 DAC Control Functions
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 0 0 0 | No Change | No Update | No Change | No operation. power-down status unchanged
0 0 0 1 | Load DAC A | No Update | No Change | Load input register A with data. DAC outputs unchanged. power-down Status unchanged
0 0 1 0 | Load DAC B | No Update | No Change | Load input register B with data. DAC outputs unchanged. power-down status unchanged
0 0 1 1 | - | - | - | Reserved
0 1 0 0 | - | - | - | Reserved
0 1 0 1 | - | - | - | Reserved

## Slide 30: LTC1661 DAC Control Functions (Cont.)
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
0 1 1 0 | - | - | - | Reserved
0 1 1 1 | - | - | - | Reserved
1 0 0 0 | No Change | Update Outputs | Wake | Load both DAC Regs with existing contents of input Regs. Outputs update. Part wakes up
1 0 0 1 | Load DAC A | Update Outputs | Wake | Load input Reg A. Load DAC Regs with new contents of input Reg A and existing contents of Reg B. Outputs update.
1 0 1 0 | Load DAC B | Update Outputs | Wake | Load input Reg B. Load DAC Regs with existing contentsof input Reg A and new contents of Reg B. Outputs update

## Slide 31: LTC1661 DAC Control Functions (Cont.)
A3 A2 A1 A0 | Interrupt Register | DAC Register | Power Down Status | Comments
1 0 1 1 | - | - | - | Reserved
1 1 0 0 | - | - | - | Reserved
1 1 0 1 | No Change | No Update | Wake | Part wakes up. Input and DAC Regs unchanged. DAC outputs reflect existing contents of DAC Regs
1 1 1 0 | No Change | No Update | Sleep | Part goes to sleep. Input and DAC Regs unchanged. DAC outputs set to high impedance state
1 1 1 1 | Load ADCs A, B with same 10-bit code | Update Outputs | Wake | Load both input Regs. Load both DAC Regs with new contents of input Regs. Outputs update. Part wakes up

## Slide 32: Connecting LTC1661 to the Microcontroller

## Slide 33: The Generated sawTooth waveform